## Slide 1: Crash data at NYC DOT
October 2018

## Slide 2: OUTLINE
Crash data
nyc.gov/dot
1 | Overview
2 | Mapping
3 | Pitfalls
4 | Use cases

## Slide 3: overview
Crash data flow
Primary datasets (NYPD & NYSDOT)
  do not agree on basic info
  Do not share ID#s

## Slide 4: Common problems
Location reporting
Accuracy
Completeness

## Slide 5: NYSDOT
Severity
NYSDOT does QA and Geocoding
Includes most of MV104 Report
Can be linked to MV104
Accessible via Safety Data Viewer (depending on need)
Includes motorist reports
Includes registration info from DMV (ex. TLC)
Data 1-2 years behind
Schema design
Unmapped cases
High volume of unknowns
Errors
Includes motorist reports
Pros
Cons

## Slide 6: NYPD TAMS
Updated daily
Consistent 1998-2016
some details added (after requested) +/- 2015 – present
Can request MV104 from NYPD using ID# (2016 – present)
Available in open data
Has license plate
Will end in 2019
  2016-2018 is temp solution from FORMS data
Limited fields
All crashes mapped to intersection
Mapping issues
Mapped to street network at the time of the crash (not the current map)
Pros
Cons

## Slide 7: NYPD FORMS
Updated daily
Modified when errors are found
Full MV104 report data
Includes midblock locations
Severity can be calculated
Includes Non-MV bike crashes
Includes coordinates and address info
Has license plate
Only available from 2016
Only reliable from 2017
Requires reverse geocode
Includes midblock locations
Geographic errors
Mapped to street network at the time of the crash (not the current map)
Includes uninvolved people
Includes Non-MV bike crashes
Issue resolution may require DOITT, NYPD, IBM, and IBI
Pros
Cons

## Slide 8: Mapping – all data
Crash location descriptions are insufficiently specific (all data sets)
Problematic locations
  Parks
  Highways & ramps
  Bridges
Street network changes
Intersection crashes are related to the intersection node as well as all related segments

## Slide 9: Common pitfalls
Using wrong (or mixed) versions of street network
Mixing NYPD and NYSDOT data
Using KSI where data is not available in both NYSDOT and Fatality data
Severity ambiguity with more than 1 victim (NYSDOT)
Taxi/livery is a registration type not a vehicle type
Not accounting for unknowns (ex. Exactly midnight in crash time)
Collision type for bike/ped crashes
X/Y vs. ST_X/ST_Y
Exclude = 0
Make sure field / value is used at appropriate frequencies prior to use
NYPD mapping pre/post 2016
FORMS victim table includes non-injured people (registrants, witnesses, etc)

## Slide 10: Typical uses
Before / after (NYPD)
Ranking (NYSDOT + Fatality)
VZ priority info (NYSDOT + Fatality)
Project / program analysis (SIP, Bikes, trucks etc)
Research studies (seniors, left turn, etc)
Press requests

## Slide 11: Basic queries
Injuries by mode (citywide) - NYPD

## Slide 12: Basic queries
Injuries by mode (citywide) - NYSDOT

## Slide 13: Basic queries
Injuries by mode at intersection – NYPD TAMS

## Slide 14: Basic queries
Injuries by mode at intersection – NYPD FORMS

## Slide 15: Basic queries
Injuries by mode at intersection - NYSDOT

## Slide 16: Basic queries
Child Ped injuries in the Bronx - NYPD

## Slide 17: Basic queries
Child Ped injuries in the Bronx - NYSDOT

## Slide 18: Basic queries
Child Passengers injuries in the Bronx - NYPD

## Slide 19: Basic queries
Child Passengers injuries in the Bronx - NYSDOT

## Slide 20
Questions?
Thank you!
NYCDOT
nyc_dot
nyc_dot
NYCDOT